## Slide 1: Digital Design & Computer Arch. Lecture 21: Memory Overview, Organization & Technology
Prof. Onur Mutlu
ETH Zürich
Spring 2023
12 May 2023

## Slide 2: Extra Credit Assignment 3: Amdahl’s Law
Paper review
  G. M. Amdahl, “Validity of the single processor approach to achieving large scale computing capabilities,” AFIPS 1967.
Optional Assignment – for 1% extra credit
  Write a 1-page review
  Upload PDF file to Moodle – Deadline: June 15
Strongly recommended that you follow my guidelines for (paper) review

## Slide 3: Readings for This Lecture and Next
Memory Hierarchy and Caches
Highly Recommended
  H&H Chapters 8.1-8.3
  Refresh: P&P Chapter 3.5
  Kim & Mutlu, “Memory Systems,” Computing Handbook, 2014.
    https://people.inf.ethz.ch/omutlu/pub/memory-systems-introduction_computing-handbook14.pdf
Recommended
  An early cache paper by Maurice Wilkes
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.

## Slide 4: We Are Done With This…
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Systolic Arrays
Decoupled Access Execute
SIMD Processing (Vector and Array processors)
Graphics Processing Units (GPUs)
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 5: Approaches to (Instruction-Level) Concurrency
Pipelining
Fine-Grained Multithreading
Out-of-order Execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Systolic Arrays
Decoupled Access Execute
SIMD Processing (Vector and Array processors, GPUs)
Now you are very familiar with
many processing paradigms

## Slide 6: Approaches to (Instruction-Level) Concurrency
Pipelining
Fine-Grained Multithreading
Out-of-order Execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Systolic Arrays
Decoupled Access Execute
SIMD Processing (Vector and Array processors, GPUs)
Food for thought:
tradeoffs of these different processing paradigms

## Slide 7: Tradeoffs of Processing Paradigms
Food for thought:
tradeoffs of these different processing paradigms
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 8: Tradeoffs of Processing Paradigms
Food for thought:
what determines the widespread success of a paradigm
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 9: Let Us Now Take A Step Back

## Slide 10: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 11: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 12: Recall: What is A Computer?
We will cover all three components
Memory
(program
and data)
I/O
Processing
control
(sequencing)
datapath

## Slide 13: Memory Is Critically Important

## Slide 14: Memory in a Modern System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER
AMD Barcelona, 2006

## Slide 15: A Large Fraction of Modern Chips is Memory
Source: https://www.anandtech.com/show/16252/mac-mini-apple-m1-tested
Apple M1, 2021

## Slide 16: A Large Fraction of Modern Systems is Memory
https://www.gsmarena.com/apple_announces_m1_ultra_with_20core_cpu_and_64core_gpu-news-53481.php
Apple M1 Ultra System (2022)
DRAM
DRAM
A lot of
SRAM
Storage
Storage

## Slide 17: A Large Fraction of Modern Systems is Memory
By Moshen - http://en.wikipedia.org/wiki/Image:Pentiumpro_moshen.jpg, CC BY-SA 2.5, https://commons.wikimedia.org/w/index.php?curid=2262471
Processor chip
Level 2 cache chip
Multi-chip module package
Intel Pentium Pro, 1995

## Slide 18: A Large Fraction of Modern Systems is Memory
https://download.intel.com/newsroom/kits/40thanniversary/gallery/images/Pentium_4_6xx-die.jpg
L2 Cache
Intel Pentium 4, 2000

## Slide 19: A Large Fraction of Modern Systems is Memory
https://wccftech.com/amd-ryzen-5000-zen-3-vermeer-undressed-high-res-die-shots-close-ups-pictured-detailed/
AMD Ryzen 5000, 2020
Core Count:
8 cores/16 threads
L1 Caches:
32 KB per core
L2 Caches:
512 KB per core
L3 Cache:
32 MB shared

## Slide 20: AMD’s 3D Last Level Cache (2021)
https://youtu.be/gqAYMx34euU
https://www.tech-critter.com/amd-keynote-computex-2021/
https://community.microcenter.com/discussion/5134/comparing-zen-3-to-zen-2
Additional 64 MB L3 cache die stacked on top of the processor die
- Connected using Through Silicon Vias (TSVs)
- Total of 96 MB L3 cache
AMD increases the L3 size of their 8-core Zen 3 processors from 32 MB to 96 MB
Notes: CCD = Core Chiplet Die
Structural silicon is used to equalize the height and facilitate heat dissipation from the cores.

## Slide 21: A Large Fraction of Modern Systems is Memory
https://www.it-techblog.de/ibm-power10-prozessor-mehr-speicher-mehr-tempo-mehr-sicherheit/09/2020/
IBM POWER10,
2020
Cores:
15-16 cores,
8 threads/core
L2 Caches:
2 MB per core
L3 Cache:
120 MB shared

## Slide 22: A Large Fraction of Modern Systems is Memory
https://www.tomshardware.com/news/infrared-photographer-photos-nvidia-ga102-ampere-silicon
Nvidia Ampere, 2020
Cores:
128 Streaming Multiprocessors
L1 Cache or Scratchpad:
192KB per SM
Can be used as L1 Cache and/or Scratchpad
L2 Cache:
40 MB shared

## Slide 23: Cerebras’s Wafer Scale Engine (2019)
Cerebras WSE
1.2 Trillion transistors
46,225 mm2
Largest GPU
21.1 Billion transistors
815 mm2
The largest ML accelerator chip
400,000 cores
18 GB of on-chip memory
9 PB/s memory bandwidth
NVIDIA TITAN V
https://www.anandtech.com/show/14758/hot-chips-31-live-blogs-cerebras-wafer-scale-deep-learning
https://www.cerebras.net/cerebras-wafer-scale-engine-why-we-need-big-chips-for-deep-learning/
Notes: The Wafer-Scale Engine is the most massive AI chip ever produced and packs a whopping 400,000 cores in a 46,225mm2 footprint.

## Slide 24: Cerebras’s Wafer Scale Engine-2 (2021)
Cerebras WSE-2
2.6 Trillion transistors
46,225 mm2
Largest GPU
54.2 Billion transistors
826 mm2
NVIDIA Ampere GA100
https://cerebras.net/product/#overview
The largest ML accelerator chip
850,000 cores
40 GB of on-chip memory
20 PB/s memory bandwidth

## Slide 25: Memory System: Most of the Platform
Storage
Most of the system is dedicated to storing and moving data
Yet, system is still bottlenecked by memory

## Slide 26: Memory is Critical for Performance
We have seen it many times in this course
Load-related stalls in pipelining
  Even with magic “1-cycle” memory assumption
Load/store handling in OoO execution processors
OoO execution and memory latency tolerance
VLIW stalls due to long-latency memory operations
VLIW memory bank disambiguation in compilers
Many memory banks needed in SIMD processors
  SIMD vector processing performance example
GPU register files and high-bandwidth memory systems
High-bandwidth memory for modern systolic arrays
Fine-grained multithreading to tolerate memory latency
…

## Slide 27: The Reason
Computing
is Bottlenecked by Data

## Slide 28: Computation is Bottlenecked by Memory
Important workloads are all data intensive
  ML/AI, Genomics, Data Analytics, Databases, Graph Analytics, …
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate much more than we can process

## Slide 29: Huge Demand for Performance & Efficiency
Source: https://youtu.be/Bh13Idwcb0Q?t=283

## Slide 30: Application Perspective

## Slide 31: Memory Is Critical for Performance (I)
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 32: Memory Is Critical for Performance (I)
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Memory → bottleneck

## Slide 33: Memory Is Critical for Performance (II)
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 34: Memory Is Critical for Performance (II)
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Memory → bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 35: Data is Key for Modern & Future Workloads
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 36
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 37
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Memory → bottleneck
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 38: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version]
Oxford Nanopore MinION

## Slide 39: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION
Memory → bottleneck

## Slide 40: We Need Faster & Scalable Genome Analysis
Predicting the presence and relative abundance of microbes in a sample
Understanding genetic variations, species, evolution, …
Rapid surveillance of disease outbreaks
Developing personalized medicine
And, many, many other applications …
Notes: Knowing what organisms are present in a given environmental sample and how abundant are they

## Slide 41: Problems with (Genome) Analysis Today
Special-Purpose Machine
for Data Generation
General-Purpose Machine
for Data Analysis
FAST SLOW
Slow and inefficient processing capability
This picture is similar for many “data generators & analyzers” today
Large amounts of data movement

## Slide 42: Future of Genome Sequencing & Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 43: Accelerating Genome Analysis
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 44: Beginner Reading on Genome Analysis
Mohammed Alser, Joel Lindegger, Can Firtina, Nour Almadhoun, Haiyu Mao, Gagandeep Singh, Juan Gomez-Luna, Onur Mutlu
“From Molecules to Genomic Variations to Scientific Discovery: Intelligent Algorithms and Architectures for Intelligent Genome Analysis”
Computational and Structural Biotechnology Journal, 2022
[Source code]
https://arxiv.org/pdf/2205.07957.pdf

## Slide 45: FPGA-based Near-Memory Analytics
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), 2021.

## Slide 46: Near-Memory Acceleration using FPGAs
IBM POWER9 CPU
HBM-based FPGA board
OCAPI
Source: AlphaData
Source: IBM
Near-HBM FPGA-based accelerator
Two communication technologies: CAPI2 and OCAPI
Two memory technologies: DDR4 and HBM
Two workloads: Weather Modeling and Genome Analysis
Notes: To this end we build a [CLICK] near-HBM FPGA based accelerator which is connected to a server-grade IBM POWER9-based CPU system

## Slide 47: Performance & Energy Greatly Improve
5-27× performance vs. a 16-core (64-thread) IBM POWER9 CPU
HBM alleviates memory bandwidth contention vs. DDR4
12-133× energy efficiency vs. a 16-core (64-thread) IBM POWER9 CPU
Notes: [CLICK]

## Slide 48: GenASM Acceleration Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 49: Scrooge: Overcoming GenASM Limitations
Joël Lindegger, Damla Senol Cali, Mohammed Alser, Juan Gómez-Luna, Nika Mansouri Ghiasi, and Onur Mutlu, "Scrooge: A Fast and Memory-Frugal Genomic Sequence Aligner for CPUs, GPUs, and ASICs" Bioinformatics, [published online on] 24 March 2023. [Online link at Bioinformatics Journal] [arXiv preprint] [Scrooge Source Code]
https://arxiv.org/pdf/2208.09985.pdf

## Slide 50: In-Storage Genome Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)] [Talk Video (17 minutes)]

## Slide 51: Accelerating Sequence-to-Graph Mapping
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 52: More on Fast & Efficient Genome Analysis …
https://www.youtube.com/watch?v=NCagwf0ivT0

## Slide 53: Detailed Lectures on Genome Analysis
Computer Architecture, Fall 2020, Lecture 3a
  Introduction to Genome Sequence Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=CrRb32v7SJc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=5
Computer Architecture, Fall 2020, Lecture 8
  Intelligent Genome Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=ygmQpdDTL7o&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=14
Computer Architecture, Fall 2020, Lecture 9a
  GenASM: Approx. String Matching Accelerator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=XoLpzmN-Pas&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=15
Accelerating Genomics Project Course, Fall 2020, Lecture 1
  Accelerating Genomics (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=rgjl8ZyLsAg&list=PL5Q2soXY2Zi9E2bBVAgCqLgwiDRQDTyId
https://www.youtube.com/onurmutlulectures

## Slide 54: Genomics Course (Fall 2022)
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=bioinformatics
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=bioinformatics
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=nA41964-9r8&list=PL5Q2soXY2Zi8tFlQvdxOdizD_EhVAMVQV
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=DEL_5A_Y3TI&list=PL5Q2soXY2Zi8NrPDgOR1yRU_Cxxjw-u18
Project course
  Taken by Bachelor’s/Master’s students
  Genomics lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 55: Performance Perspective

## Slide 56: It’s the Memory, Stupid!
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
http://cva.stanford.edu/classes/cs99s/papers/architects_look_to_future.pdf

## Slide 57: The Performance Perspective
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 58: The Performance Perspective
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors" Proceedings of the 9th International Symposium on High-Performance Computer Architecture (HPCA), pages 129-140, Anaheim, CA, February 2003. Slides (pdf)
  One of the 15 computer arch. papers of 2003 selected as Top Picks by IEEE Micro. HPCA Test of Time Award (awarded in 2021). [Lecture Slides (pptx) (pdf)] [Lecture Video (1 hr 54 mins)] [Retrospective HPCA Test of Time Award Talk Slides (pptx) (pdf)] [Retrospective HPCA Test of Time Award Talk Video (14 minutes)]

## Slide 59: The Memory Bottleneck
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Effective Alternative to Large Instruction Windows" IEEE Micro, Special Issue: Micro's Top Picks from Microarchitecture Conferences (MICRO TOP PICKS), Vol. 23, No. 6, pages 20-25, November/December 2003.

## Slide 60: The Memory Bottleneck
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 61: The Memory Bottleneck
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 62: An Informal Interview on Memory
Madeleine Gray and Onur Mutlu, "‘It’s the memory, stupid’: A conversation with Onur Mutlu" HiPEAC info 55, HiPEAC Newsletter, October 2018. [Shorter Version in Newsletter] [Longer Online Version with References]

## Slide 63: Energy Perspective

## Slide 64: Data Movement vs. Computation Energy
Dally, HiPEAC 2015

## Slide 65: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 66: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.

## Slide 67: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.
6400X
A memory access consumes 6400X
the energy of a simple integer addition

## Slide 68: Data Movement vs. Computation Energy
32-bit Operation | Energy (pJ) | ADD (int) Relative Cost
ADD (int) | 0.1 | 1
ADD (float) | 0.9 | 9
Register File | 1 | 10
MULT (int) | 3.1 | 31
MULT (float) | 3.7 | 37
SRAM Cache | 5 | 50
DRAM | 640 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.
A memory access consumes ~6400X
the energy of an integer addition

## Slide 69: Memory is Critical for Energy
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 70: Memory is Critical for Energy
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]
> 90% of the total system energy
is spent on memory in large ML models

## Slide 71: Processing in Memory: Faster & Low Energy
https://ethz.ch/en/industry/industry/news/data/2022/03/mehr-daten-schneller-und-energiesparender-verarbeiten.html

## Slide 72: Tutorial on Processing in Memory
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=4x9nujJtqjM

## Slide 73: Reliability, Security, Safety Perspectives

## Slide 74: Memory is Critical for Reliability
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
As memory
capacity increases, system reliability reduces

## Slide 75: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 76: Infrastructures to Understand Such Issues
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 77: Memory Testing Infrastructures
* SoftMC [Hassan+, HPCA’17] enhanced for DDR4
Notes: We implement U-TRR using SoftMC, an FPGA-based infrastructure with precise temperature control which we enhanced for DDR4

## Slide 78: Updated Memory Testing Infrastructure
  FPGA-based SoftMC (Xilinx Virtex UltraScale+ XCU200)
Fine-grained control over DRAM commands,
timing (±1.5ns), temperature (±0.1°C ),
and voltage (±1mV)
*Hassan et al., "SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies," in HPCA, 2017. [Available on GitHub: https://github.com/CMU-SAFARI/SoftMC]
*
Notes: We use an FPGA-based experimental setup programmed with a modified version of SoftMC [CLICK]
We control the chip temperature using a pair of heaters [CLICK] connected to a temperature controller [CLICK]
We supply the wordline voltage using the VPP power rail from an external power supply [CLICK]
This infrastructure provides fine-grained control over DRAM commands, timing parameters, temperature, and wordline voltage [CLICK]
=======

## Slide 79: A Curious Phenomenon [Kim et al., ISCA 2014]
One can
predictably induce errors
in most DRAM memory chips
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.

## Slide 80: DRAM RowHammer
A simple hardware failure mechanism
can create a widespread
system security vulnerability

## Slide 81: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn+, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)

## Slide 82: A RowHammer Survey Across the Stack
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version] [Slides from COSADE 2019 (pptx)] [Slides from VLSI-SOC 2020 (pptx) (pdf)] [Talk Video (1 hr 15 minutes, with Q&A)]

## Slide 83: RowHammer is Still a Security Problem
Onur Mutlu, Ataberk Olgun, and A. Giray Yaglikci, "Fundamentally Understanding and Solving RowHammer" Invited Special Session Paper at the 28th Asia and South Pacific Design Automation Conference (ASP-DAC), Tokyo, Japan, January 2023. [arXiv version] [Slides (pptx) (pdf)] [Talk Video (26 minutes)]
https://arxiv.org/pdf/2211.07613.pdf

## Slide 84: Memory is Critical for Security
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 85: The Story of RowHammer Tutorial …
https://www.youtube.com/watch?v=e6G_Vbrqr_c&list=PL5Q2soXY2Zi9uIibswgf8IfNGKYktIEos&index=4

## Slide 86: The Story of RowHammer Tutorial …
Onur Mutlu, "Security Aspects of DRAM: The Story of RowHammer" Invited Tutorial at 14th IEEE Electron Devices Society International Memory Workshop (IMW), Dresden, Germany, May 2022. [Slides (pptx)(pdf)] [Tutorial Video (57 minutes)]
https://www.youtube.com/watch?v=37hWglkQRG0

## Slide 87: 10 Years of RowHammer in 20 Minutes
Onur Mutlu, "The Story of RowHammer" Invited Talk at the Workshop on Robust and Safe Software 2.0 (RSS2), held with the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, 28 February 2022. [Slides (pptx) (pdf)]
https://www.youtube.com/watch?v=ctKTRyi96Bk

## Slide 88: Memory Is Critical for Computing

## Slide 89: Memory Is Critical for Computing
Performance
Energy
Reliability
Security & Safety
Cost
Form Factor
Quality of Service & Predictability
Sustainability
…

## Slide 90: Memory Fundamentals

## Slide 91: Memory Organization & Technology

## Slide 92: Memory (Programmer’s View)

## Slide 93: Abstraction: Virtual vs. Physical Memory
Programmer sees virtual memory
  Can assume the memory is “infinite”
Reality: Physical memory size is much smaller than what the programmer assumes
The system (system software + hardware, cooperatively) maps virtual memory addresses to physical memory
  The system automatically manages the physical memory space transparently to the programmer
+ Programmer does not need to know the physical size of memory nor manage it  A small physical memory can appear as a huge one to the programmer  Life is easier for the programmer
-- More complex system software and architecture
A classic example of the programmer/(micro)architect tradeoff
Requires indirection and mapping between virtual and physical address spaces

## Slide 94: (Physical) Memory System
You need a larger level of storage to manage a small amount of physical memory automatically
   Physical memory has a backing store: disk
We will first start with the physical memory system
For now, ignore the virtualphysical indirection
We will get back to it later, if time permits…

## Slide 95: Idealism
Instruction
Supply
Pipeline
(Instruction
Execution)
Data
Supply
- Zero latency access
- Infinite capacity
- Zero cost
- Perfect control flow
No pipeline stalls
Perfect data flow
(no reg/memory dependences)
Zero-cycle interconnect
(operand communication)
Enough functional units
Zero latency compute
Zero latency access
Infinite capacity
- Infinite bandwidth
Zero cost

## Slide 96: Ideal Memory
Zero access time (latency)
Infinite capacity
Zero cost
Infinite bandwidth (to support multiple accesses in parallel)
Zero energy

## Slide 97: Quick Overview of Memory Arrays

## Slide 98: How Can We Store Data?
Flip-Flops (or Latches)
  Very fast
  Very expensive (one bit costs tens of transistors)
Static RAM (we will describe it soon)
  Relatively fast
  Expensive (one bit costs 6+ transistors)
Dynamic RAM (we will describe it soon)
  Slower, reading and charge leakage destroys content (refresh), needs special process for manufacturing (due to capacitor)
  Cheap (one bit costs only one transistor plus one capacitor)
Other storage technology (flash memory, hard disk, tape)
  Much slower, special manufacturing needed, non-volatile
  Very cheap (one transistor stores many bits or no transistors involved)

## Slide 99: Array Organization of Memories
Goal: Efficiently store large amounts of data
  A memory array (stores data)
  Address selection logic (selects one row of the array)
  Readout circuitry (reads data out)
An M-bit value can be read or written at each unique N-bit address
  All values can be accessed, but only M-bits at a time
  Access restriction allows more compact organization

## Slide 100: Recall: A Bigger Memory Array (4 locations X 3 bits)
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[1:0]
WE
Address Decoder
Multiplexer
DDCA Lecture 5
https://www.youtube.com/watch?v=AFK2nL8aaZk&list=PL5Q2soXY2Zi-EImKxYYY1SZuGiOAOBKaf&index=6

## Slide 101: Memory Arrays
Two-dimensional array of bit cells
  Each bit cell stores one bit
An array with N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (can be number of “words”)
  Width: number of columns (can be the “word” size)
  Array size: depth × width (rows x columns) = 2N × M

## Slide 102: Memory Array Example
22 × 3-bit array
Number of rows: 4
Row size: 3 bits
For example, the 3-bit data stored at row 10 is 100

## Slide 103: Larger and Wider Memory Array Example

## Slide 104: Memory Array Organization (I)
Storage nodes in one column connected to one bitline
Address decoder activates only ONE wordline
Content of one line of storage available at output

## Slide 105: Memory Array Organization (II)
Storage nodes in one column connected to one bitline
Address decoder activates only ONE wordline
Content of one line of storage available at output
10
1
0
0
Active wordline

## Slide 106: How is Access Controlled?
Access transistors (that are configured as switches) connect the bit storage to the bitline
Access is controlled by the wordline
DRAM
SRAM

## Slide 107: Building Larger Memories
Requires larger memory arrays
Large  slow
How do we make the memory large without making it too slow?
Idea: Divide the memory into smaller arrays and interconnect the arrays to input/output buses
  Large memories are hierarchical array structures
  DRAM: Channel  Rank  Bank  Subarrays  Mats

## Slide 108: General Principle: Interleaving (Banking)
Interleaving (banking)
  Problem: a single monolithic large memory array takes long to access and does not enable multiple accesses in parallel
  Goal: Reduce the latency of memory array access and enable multiple accesses in parallel
  Idea: Divide a monolithic large array into multiple banks that can be accessed independently (in the same cycle or in consecutive cycles)
    Each bank is smaller than the entire memory storage
    Accesses to different banks can be overlapped
  A Key Issue: How do you map data to different banks? (i.e., how do you interleave data across banks?)

## Slide 109: Recall: Memory Banking
Memory is divided into banks that can be accessed independently; banks share address and data buses (to reduce memory chip pins)
Can start and complete one bank access per cycle
Can sustain N concurrent accesses if all N go to different banks
Bank
0
Bank
1
MDR
MAR
Bank
2
Bank
15
MDR
MAR
MDR
MAR
MDR
MAR
Data bus
Address bus
CPU
DDCA Lecture 19
https://www.youtube.com/watch?v=gkMaO3yJMz0&list=PL5Q2soXY2Zi-EImKxYYY1SZuGiOAOBKaf&index=24

## Slide 110: Generalized Memory Structure

## Slide 111: Generalized Memory Structure
Kim+, “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.
Lee+, “Decoupled Direct Memory Access,” PACT 2015.

## Slide 112: Cutting Edge: 3D-Stacking of Memory & Logic
Logic
Memory
Other “True 3D” technologies
under development

## Slide 113: The DRAM Subsystem A Top-Down View

## Slide 114: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 115: The DRAM Subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 116: Breaking down a DIMM (module)
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM

## Slide 117: Breaking down a DIMM (module)
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 118: Rank
Rank 0 (Front)
Rank 1 (Back)
Data <0:63>
CS <0:1>
Addr/Cmd
<0:63>
<0:63>
Memory channel

## Slide 119: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 120: Breaking down a Chip
Chip 0
<0:7>
8 banks
Bank 0
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 121: Breaking down a Bank
Bank 0
<0:7>
row 0
row 32k-1
...
2kB
1B
1B (column)
1B
Row-buffer
1B
...
<0:7>

## Slide 122: Digging Deeper: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:
This view of a bank is an abstraction.
Internally, a bank consists of many cells (transistors & capacitors) and other structures that enable access
to cells

## Slide 123: A DRAM Bank Internally Has Sub-Banks
Kim et al., “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.

## Slide 124: Another View of a DRAM Bank
Seshadri+, “In-DRAM Bulk Bitwise Execution Engine,” ADCOM 2020.
Logical Abstraction
Physical View

## Slide 125: More on DRAM Basics & Organization
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, 2020. [Preliminary arXiv version]
See Section 2 for comprehensive DRAM Background
https://arxiv.org/pdf/1905.09822.pdf

## Slide 126: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 127: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Channel 0
DIMM 0
Rank 0
Mapped to

## Slide 128: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 129: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 130: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 131: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 1
. . .

## Slide 132: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
. . .
8B

## Slide 133: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
A 64B cache block takes 8 I/O cycles to transfer.
During the process, 8 columns are read sequentially.
. . .

## Slide 134: Memory Technology: DRAM and SRAM

## Slide 135: Memory Technology: DRAM
Dynamic random access memory
Capacitor charge state indicates stored value
  Whether the capacitor is charged or discharged indicates storage of 1 or 0
  1 capacitor
  1 access transistor
Capacitor leaks through the RC path
  DRAM cell loses charge over time
  DRAM cell needs to be refreshed
row enable
bitline

## Slide 136: Memory Technology: SRAM
Static random access memory
Two cross coupled inverters store a single bit
  Feedback path enables the stored value to stay in the “cell” (as long as powered on)
  4 transistors for storage
  2 transistors for access
row enable
bitline
_bitline

## Slide 137: Memory Bank Organization and Operation
Read access sequence:
1. Decode row address & drive word-lines
2. Selected bits drive bit-lines
• Entire row read
3. Amplify row data
4. Decode column address & select subset of row
• Send to output
5. Precharge bit-lines
• For next access

## Slide 138: SRAM (Static Random Access Memory)
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m diff pairs
2n
n
m
1
row enable
bitline
_bitline
n+m
Read Sequence
  1. address decode
  2. drive row enable
  3. selected bit-cells drive bitlines
  (entire row is read together)
  4. differential sensing and column select
  (data is ready)
  5. precharge all bitlines
  (for next read or write)
Access latency dominated by steps 2 and 3
Cycling time dominated by steps 2, 3 and 5
  step 2 proportional to 2m
  step 3 and 5 proportional to 2n

## Slide 139: DRAM (Dynamic Random Access Memory)
row enable
_bitline
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m
2n
n
m
1
RAS
CAS
A DRAM die comprises
of multiple such arrays
Bit stored as charge on node capacitor (non-restorative)
  bit cell loses charge when read
  bit cell loses charge over time
Read Sequence
  1~3 same as SRAM
  4. a “flip-flopping” sense amp amplifies and regenerates the bitline, data bit is mux’ed out
  5. precharge all bitlines
Destructive reads
Charge loss over time
Refresh: A DRAM controller must periodically read each row within the allowed refresh time (10s of ms) such that charge is restored

## Slide 140: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 141: An Aside: Phase Change Memory
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 142: PCM-based Main Memory
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]
  How to redesign the system to tolerate PCM shortcomings
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]
  How to partition/migrate data between PCM and DRAM

## Slide 143: Reading: PCM as Main Memory: Idea in 2009
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf) One of the 13 computer architecture papers of 2009 selected as Top Picks by IEEE Micro. Selected as a CACM Research Highlight. 2022 Persistent Impact Prize.

## Slide 144: Reading: More on PCM As Main Memory
Benjamin C. Lee, Ping Zhou, Jun Yang, Youtao Zhang, Bo Zhao, Engin Ipek, Onur Mutlu, and Doug Burger, "Phase Change Technology and the Future of Main Memory" IEEE Micro, Special Issue: Micro's Top Picks from 2009 Computer Architecture Conferences (MICRO TOP PICKS), Vol. 30, No. 1, pages 60-70, January/February 2010.

## Slide 145: Intel Optane Persistent Memory (2019)
Non-volatile main memory
Based on 3D-XPoint Technology
https://www.storagereview.com/intel_optane_dc_persistent_memory_module_pmm

## Slide 146: DRAM vs. PCM
DRAM
  Faster access (capacitor)
  Lower density (capacitor less scalable)  higher cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
  Volatile (loses data at loss of power)
  No endurance problems
  Lower access energy
PCM
  Slower access (heating and cooling based ”phase change” operation)
  Higher density (phase change material more scalable)  lower cost
  No need for refresh
  Manufacturing requires less conventional processes – less mature
  Non-volatile (does not lose data at loss of power)
  Endurance problems (a cell cannot be used after N writes to it)
  Higher access energy

## Slide 147: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 148: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 149: More on Emerging Memory Technologies
https://www.youtube.com/watch?v=AlE1rD9G_YU&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=28

## Slide 150: More on Emerging Memory Technologies
https://www.youtube.com/watch?v=pmLszWGmMGQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=29

## Slide 151: More on Memory Technologies
https://www.youtube.com/watch?v=pmLszWGmMGQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=29

## Slide 152: A Bit on Flash Memory & SSDs
Flash memory was a very “doubtful” emerging technology
  for at least two decades
Proceedings of the IEEE, Sept. 2017
https://arxiv.org/pdf/1711.11427.pdf

## Slide 153: A Flash Memory SSD Controller
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.
https://arxiv.org/pdf/1711.11427.pdf

## Slide 154: Lecture on Flash Memory & SSDs
https://www.youtube.com/watch?v=rninK6KWBeM&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=47

## Slide 155: SSD Course (Spring 2023)
Spring 2023 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2023/doku.php?id=modern_ssds
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=modern_ssds
Youtube Livestream (Spring 2023):
  https://www.youtube.com/watch?v=4VTwOMmsnJY&list=PL5Q2soXY2Zi_8qOM5Icpp8hB2SHtm4z57&pp=iAQB
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=hqLrd-Uj0aU&list=PL5Q2soXY2Zi9BJhenUq4JI5bwhAMpAp13&pp=iAQB
Project course
  Taken by Bachelor’s/Master’s students
  SSD Basics and Advanced Topics
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 156: Lectures on Memory Technologies
Computer Architecture, Fall 2020, Lecture 15
  Emerging Memory Technologies (ETH, Fall 2020)
  https://www.youtube.com/watch?v=AlE1rD9G_YU&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=28
Computer Architecture, Fall 2020, Lecture 16a
  Opportunities & Challenges of Emerging Memory Tech (ETH, Fall 2020)
  https://www.youtube.com/watch?v=pmLszWGmMGQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=29
Computer Architecture, Fall 2020, Lecture 3b
  Memory Systems: Challenges & Opportunities (ETH, Fall 2020)
  https://www.youtube.com/watch?v=Q2FbUxD7GHs&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=6
https://www.youtube.com/onurmutlulectures

## Slide 157: Tutorial on Processing in Memory
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=4x9nujJtqjM

## Slide 158: Processing in Memory Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/2012.03112.pdf

## Slide 159: PIM Course (Fall 2022)
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=processing_in_memory
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=QLL0wQ9I4Dw&list=PL5Q2soXY2Zi8KzG2CQYRNQOVD0GOBrnKy
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 160: Digital Design & Computer Arch. Lecture 21: Memory Overview, Organization & Technology
Prof. Onur Mutlu
ETH Zürich
Spring 2023
12 May 2023

## Slide 161: Goal: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processors & communication units?
  software & hardware interfaces?
  system software, compilers, languages?
  algorithms & theoretical foundations?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 162: Backup Slides: Inside A DRAM Chip

## Slide 163: DRAM Module and Chip

## Slide 164: Goals in DRAM Design
Cost
Latency
Bandwidth
Parallelism
Power
Energy
Reliability
Security
…

## Slide 165: DRAM Chip
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O

## Slide 166: Sense Amplifier
enable
top
bottom
Inverter

## Slide 167: Sense Amplifier – Two Stable States
1
1
0
0
VDD
VDD
Logical “1”
Logical “0”

## Slide 168: Sense Amplifier Operation
0
VT
VB
VT > VB
1
0
VDD

## Slide 169: DRAM Cell – Capacitor
Empty State
Fully Charged State
Logical “0”
Logical “1”
1
2
Small – Cannot drive circuits
Reading destroys the state

## Slide 170: Capacitor to Sense Amplifier
1
0
VDD
1
VDD
0

## Slide 171: DRAM Cell Operation
½VDD
½VDD
0
1
0
VDD
½VDD+δ

## Slide 172: DRAM Subarray – Building Block for DRAM Chip
Row Decoder
Cell Array
Cell Array
Array of Sense Amplifiers (Row Buffer) 8Kb

## Slide 173: DRAM Bank
Row Decoder
Array of Sense Amplifiers (8Kb)
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O (64b)
Address
Address
Data

## Slide 174: DRAM Chip
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Shared internal bus
Memory channel - 8bits

## Slide 175: DRAM Operation
Row Decoder
Row Decoder
Array of Sense Amplifiers
Cell Array
Cell Array
Bank I/O
Data
1
2
ACTIVATE Row
READ/WRITE Column
3
PRECHARGE
Row Address
Column Address

## Slide 176: More on DRAM Operation: Section 2
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]
https://arxiv.org/pdf/1905.09822.pdf
See Section 2 for comprehensive DRAM Background